## Slide 1: Preprocessing & Layout Analysis for Offline Handwriting Recognition
東北大学大学院工学研究科
電子工学専攻川又研究室
Perttu Pitkänen

## Slide 2: Overview
Handwriting recognition
Preprocessing
Layout Analysis
Tests
Conclusions
Future work

## Slide 3: Handwriting recognition 1
Offline handwriting recognition (HWR) is the process of extracting text in digital form from handwritten images.
Offline recognition process can be divided into three main phases:
  Preprocessing
  Feature extraction
  Classification
Implementation done with MATLAB and its image processing toolbox

## Slide 4: Handwriting recognition 2
Preprocessing
  Image is enhanced for feature extraction phase and the detected characters are segmented from the original image.
  Layout analysis can be considered to be a part of preprocessing
Feature Extraction
  Shape describing features are extracted from previously acquired objects.
Classification
  Extracted features are used in machine learning algorithms to create the feature vector.

## Slide 5: Preprocessing 1
Most of the preprocessing is same than previously
  Image aquisition
  Noise removal
    Adaptive Wiener filter
  Binarization
    Sauvola algorithm
  Object property analysis
    Features such as holes in object, size, area or aspect ratio
    Stroke width variation
All methods need pre-defined threshold values.
Object property analysis now uses sroke width instead of other features.

## Slide 6: Stroke Width Analysis 1
One distinctive feature of text is that it consists of ”strokes”
Strokes have only a little variation in thickness.
Other objects such as images can have lot of variation in thickness.
The amount of variation can be used to distinquish text from other objects.
Dark blue represents thin stroke width and dark red thick strokes

## Slide 7: Stroke Width Analysis 2
Get image regions
Distance transform
For each pixel find distance to nearest black pixel
Get image skeleton
Make one dimensional vector V which contains all distance transform values
Calculating stroke width metric to represent the width variation.
Standard deviation of V divided by the mean value of V.
Removing values that have more variation than threshold
[6.403, 8.5440, 6.4031, 8.0623, 5.6569, 7.2801,...]
0.2360

## Slide 8: Layout Analysis
Analysing the image regions to find where the text is located and what kind of bodies of text it contains
Columns, rows, words.
Proposed method to find the areas of interest is to draw bounding boxes over the text objects, expand them in all directions and combine overlapping boxes.

## Slide 9: Bounding box expansion
= Area of interest box
In the last phase boxes that take only a small fraction of the total area are removed.

## Slide 10: Layout Analysis 2
To find rows of text the run length smearing algorithm is used.
The RLSA finds rows of black pixels and changes them to white if they are under given threshold.
The bounding box is taken for each object generated by RLSA. These bounding boxes represent the rows.
The same method is used to find individual words within rows. For words the RLSA is executed also vertically. Smaller threshold values are used.

## Slide 11: RLSA for rows
= Row box

## Slide 12: RLSA for words
Same procedure but this time the algorithm is also run vertically to get dots or other broken characters into word.
= Word box

## Slide 13: Full layout visualized
= Area of interest box
= Row box
= Word box

## Slide 14: Tests
The system is still dependant on the threshold values.
The tests goal is to find these threshold values for IAM database.

## Slide 15: Example entries in IAM handwriting database.
The database contains also metadata from each picture such as number of rows and words

## Slide 16: Test procedure
25 different handwriting samples and their metadata
Iterate through a list of tested values
With each iteration run the preprocessing and layout analysis for each image
Get the number of detected rows and words
Compare detected rows and words to the actual values
Visualize results

## Slide 17: Test results
(aja testit yhdelle kuvalle kerrallaan katotaan sitte uudestaan)

## Slide 18: Remaining problems
The row and word detection isn’t perfect
  If two rows contain overlapping characters those rows are combined as one.
  Words can be broken or two or more words are combined as one.
= Area of interest box
= Row box
= Word box
Result: Two rows and five words!

## Slide 19: Remaining problems: Overlapping characters
= Real word box (unrealized)