Handwriting recognition
Implementation

The system implemetation is completed using MATLAB with image processing toolbox.
### Preprocessing
1. Image acquisition. Accepts jpg, png and gif images to name a few.
2. Image conversion to rgb. Matlab function rgb2gray(I) eliminates hue and saturation information and keeps lumination.
3. Conversion to grayscale.
4. Noise removal. This is done with n x m adaptive wiener filter.
  For this purpose 3x3 filter was chosen. For small filter size less blur occurs.
5. Histogram equalization. May not be necessary. Can often result in worse binarization when irrelevant objects are enhanced. For example if the text is on squared paper the grid is enhanced making it visible after binarization.
6. Binarization. Sauvola algorithm is used as it is one of the most popular binarization methods and it has been developed specifically for document image binarization.
  sauvola(I,[M, N],threshold, padding)
  I = image
  [M,N] = MxN neighbourhood used to determine the adaptive threshold for that area.
  threshold (k) = user defined parameter. ???? Chosen value k=0.2 gives good results.
  padding = the method to handle border pixels. Default mode is 'replicate' which replicates the border pixels.
7. Morphological opening. This is used to remove objects which are outside of given threshold values. Helps to remove noise that couldn't be removed previously and to remove irrelevant big objects such as drawings.
8. Segmentation. To extract the objects the function bwboundaries(BW,conn,options) is used. Where BW = binary image, conn=connectivity 4 or 8 connectivity with neighbor pixels, options = option to choose modes 'holes' or 'noholes'. This defines whether the holes are included. For the purpose of handwriting recognition the arguments are as follows: 8-connectivity with 'holes' mode selected. The holes must be included as many character have holes in them e.g. the letter 'O'.

For preprocessing it is important to adjust the image so that it is suitable for handwriting recognition. For this purpose the image file should be binarized as well as possible. Prior the binarization noise should be removed and the image should be in grayscale. This implementation removes noise with 3x3 adaptive wiener filter. The hisogram equalization is problematic because on the other hand it can improve the binarization result but it can also make it worse if the contrast is sufficient in the beginning. In this case irrelevant objects such as paper texture may appear darker.
The image might have other elements that are irrelevant to text recognition such as pictures or drawings so these elements should be ignored. For this purpose the image is analyzed and the blobs having area smaller or bigger than selected threshold values should not be included in the segmentation process. This also helps to remove some noise that the previous filter couldn't remove. The threshold values should be chosen carefully as they highly depend on the image resolution and text size. If incorrect values are chosen relevant text may not be analyzed or irrelevant bjects are included.